## Slide 1: Lecture 4
Muhammad Irfan Ishaq

## Slide 2: Lecture Outline
Basic Computer Organization
Intel Architecture 32-bit (IA-32) Registers and Instruction Execution Cycle
x86 Processor Architecture

## Slide 3: Book Chapter
“Assembly Language for x86 processors”
Author “Kip R. Irvine”
6th Edition
Chapter 2
  Section 2.1
  Section 2.1.2
  Section 2.2
  Section 2.2.4
  Section 2.3

## Slide 4: Organization and Architecture
Computer Architecture
  Attributes of a computer that have a direct impact on the logical program execution
  e.g. I/O mechanisms, memory addressing techniques
Computer Organization
  Operational units and their interconnection that realizes the architectural specifications
  e.g. control signals, interconnection between computer and its peripherals

## Slide 5: Basic Computer Organization (1/2)
Computer has 3 main components
  Processor, also called Central Processing Unit (CPU)
  Memory and Storage Devices
  I/O Devices
These components communicate with each other through
  Data Bus
  I/O Bus
  Address Bus
  Control Bus

## Slide 6: Basic Computer Organization (2/2)
Memory Storage Unit
I/O Device #1
I/O Device #2
Central
Processing Unit
(CPU)
ALU | CU | CLOCK
I/O Bus
Address Bus
Control Bus
Registers
Data Bus

## Slide 7: Central Processing Unit (CPU)
Generally called Processor
Contains
  Clock
  Registers
  Arithmetic Logic Unit (ALU)
    Performs arithmetic and logic instructions
  Control Unit (CU)
    Generates the control signals required to execute the instructions

## Slide 8: Clock (1/2)
Clock cycle is basic unit of time for machine instructions
Synchronizes Processor and Bus operations
Clock cycle = Clock period = 1/(Clock Rate)
Clock Rate = Clock Frequency = Cycles per sec
  1 Hz clock produces 1 Clock Cycle in 1 second
  1 KHz clock produces 1000 Clock Cycles in 1 second
  1 MHz clock produces 1,000,000 cycles in 1 second
  1 GHz clock produces 1,000,000,000 cycles in 1 second

## Slide 9: Clock (2/2)
Clock Frequency | Clock Period (sec) | Time to execute one instruction
1 Hz | 1 | 1 sec
1 KHz | 0.001 | 1 ms (millisecond)
1 MHz | 0.000,001 | 1 μs (microsecond)
1 GHz | 0.000,000,001 | 1 ns (nanosecond)
1
0
One Cycle

## Slide 10: Memory (1/2)
Ordered sequence of bytes
  Sequence number is called memory address
Byte addressable memory
  Each byte has a unique address
Physical address space
  Determined by the address bus width
  Pentium has 32-bit address bus
    Physical address space of Pentium = 232 bytes = 4 GB
  Itanium with 64-bit address bus can support up to 264 bytes of physical address space

## Slide 11: Memory (2/2)
Address of location to be read/written is placed on the address bus
Data to be read/written is placed on the data bus by memory/processor
Two control signals read and write decide the reading or writing operations
Memory Unit
Address
Read
Write
Data

## Slide 12: Physical Address Space
Address
in decimal
Address
in hex
0
1
2
232-1
00000000
00000001
00000002
FFFFFFFD
FFFFFFFE
FFFFFFFF
Address space is the set of addressable memory locations (bytes)

## Slide 13: Reading from Memory
Multiple clock cycles are required
Memory responds much more slowly than CPU
Reading process is carried out in this way
  Address is placed on the address bus
  Read Line (RD) goes low indicating that processor wants to read
  CPU waits for memory to respond
  Read Line (RD) goes high indicating that data has been placed on the data bus

## Slide 14: Memory Read and Write Cycles
In Read Cycle, the Processor
  places address on address bus
  asserts the memory read control signal
  waits for memory to place data on the data bus
  reads the data from data bus
  drops the memory read signal
In Write Cycle, the Processor
  places address on the address bus
  asserts the memory write control signal
  places the data on the data bus
  waits for memory to store the data
  drops the memory write signal

## Slide 15: Reading from Memory

## Slide 16: Memory Hierarchy
Registers
  Fastest storage elements
Cache Memory
  Stores recently used instructions
Main Memory
Magnetic Disk
  Stores data permanently
Magnetic Tape
Magnetic Tape
Magnetic Disk
CD-ROM
CD-RW
DVD-RW
Off-line Storage
Outboard
Storage
Inboard
Storage
Main Memory
Cache
Regis-ters
Lower cost per Byte
Higher Speed, Smaller Size

## Slide 17: Registers
Very high speed memory units inside CPU
Can be categorized into
  General Purpose Registers
  Segment Registers
  Instruction Pointer
  EFLAGS Register
    Control Flags
    Status Flags

## Slide 18: General Purpose Registers
Used primarily for arithmetic and data movement
Eight 32-bit Extended general purpose registers
Register | Description | Specialized Usage
EAX | Accumulator | Used in mul and div instruction
EBX | Base | 
ECX | Counter | Used in LOOP instruction
EDX | Data | 
EBP | Base Pointer | Used to reference local variables on stack
ESP | Stack Pointer | Points at top of the stack, used by PUSH and POP
ESI | Source Index | Used by high speed memory transfer instruction
EDI | Destination Index | Used by high speed memory transfer instruction

## Slide 19: Accessing Parts of Registers (1/2)
Portions of General Purpose Registers can also be accessed
  Lower 16 bits of EAX are named AX
  AX can further be divided into
    AL = Lower 8 bits
    AH = Higher 8 bits
EAX
AX
AH
AL
32 bits
16 bits
8 bits
0
7
8
15
16
31
8 bits

## Slide 20: Accessing Parts of Registers (2/2)
  EAX, EBX, ECX, EDX can be accessed at word and byte level
  EBP, ESP, ESI, EDI can be accessed at word level
32-bit | 16-bit | 8-bit Higher | 8-bit Lower
EAX | AX | AH | AL
EBX | BX | BH | BL
ECX | CX | CH | CL
EDX | DX | DH | DL
32-bit | 16-bit Lower
ESP | SP
EBP | BP
ESI | SI
EDI | DI

## Slide 21: Segment Registers (1/2)
Six 16-bit segment registers
Indicate base addresses of pre-assigned memory areas
An assembly program usually contains 3 segments
  Stack Segment: holds local function variables and function parameters
  Data Segment: holds variables
  Code Segment: holds program instructions

## Slide 22: Segment Registers (2/2)
SS = Stack Segment
DS = Data Segment
CS = Code Segment
3 extra segment registers
  ES, FS, GS (Extra Segment)
SS
DS
CS
ES
FS
GS

## Slide 23: Instruction Pointer
Represented by EIP
Also called Program Counter (PC)
Contains the address of next instruction to be executed
Its value changes with the execution of program
Certain machine instructions influence the value of EIP

## Slide 24: EFLAGS
EFLAGS register consists of individual binary bits
Can be categorized into
  Control Flags: control the operation of CPU
  Status Flags: reflect the outcome of arithmetic and logical operations
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | ID | VIP | VIF | AC | VM | RF | 0 | NT | IOPL | OF | DF | IF | TF | SF | ZF | 0 | AF | 0 | PF | 1 | CF

## Slide 25: Status Flags
Arithmetic and Logical operations set/reset them
Status Flags are
  Carry Flag (CF): set when unsigned arithmetic operation produces a carry
  Overflow Flag (OF): sets when signed arithmetic result is out of range
  Sign Flag (SF): sets when result of operation is –ve
  Zero Flag (ZF): sets when result of operation is zero
  Auxiliary Flag (AF): sets when there is a carry from bit 3 to bit 4
  Parity Flag (PF): sets when parity is even

## Slide 26: Floating Point Unit (FPU)
FPU performs high speed floating point operations
Integrated into main processor chip from Intel486 onward
Eight 80-bit floating point data registers
All arranged as a stack
ST(7)
ST(1)
ST(0)
ST(3)
ST(2)
ST(5)
ST(4)
ST(6)

## Slide 27: Instruction Execution Cycle (1/2)
A program is loaded into memory before execution
Instruction Pointer (IP) contains the address of next instruction to be executed
Instruction Queue contains the group of instructions about to be executed
Three basic steps in execution of a machine instruction
  Fetch
  Decode
  Execute
Two more steps if the instruction uses an operand located in memory
  Fetch Operand
  Store Output

## Slide 28: Instruction Execution Cycle (2/2)
Order of steps when instruction uses an operand located in memory
  Instruction Fetch (IF)
  Instruction Decode (ID)
  Operand Fetch from Memory (OF)
  Instruction Execute (IE)
  Write Back in Memory (WB)
Instruction Execution Cycle (IEC) is the combination of all above operations

## Slide 29: Instruction Fetch
Program Counter (PC) or IP holds address of next instruction to be executed
Processor fetches instruction from memory pointed to be PC
Increment PC to the next instruction
Fetching operation concludes here

## Slide 30: Instruction Decode
Control Unit (CU) determines the function of the instruction
Instruction’s input operands are passed to ALU
Signals sent to ALU to perform the desired operation

## Slide 31: Operand Fetch from Memory
Sometimes instructions may involve some operands located in memory
In this case, data should be retrieved from memory
The CU uses a memory read operation
CU copies these operands into Instruction Registers which are invisible to user programs

## Slide 32: Instruction Execute
The instruction is ready for execution at this stage
ALU executes the instruction
ALU updates the status flags providing information about the result

## Slide 33: Write Back in Memory
The output may be required to save in memory for future uses
CU performs a write operation to save this output into memory

## Slide 34: IEC Graphical View
Instruction Fetch
Instruction Decode
Operand Fetch
Instruction Execute
Write Back in Memory
Obtain instruction from Instruction Queue
Determine required action to be executed
Locate and obtain operand from memory location
Compute the required operation
Deposit results in the storage for future use
Infinite Cycle

## Slide 35: Intel Microprocessors
Size of data bus is significant in processor evolution
How to transfer 32-bit data with an 8-bit data bus?

## Slide 36: Evolution of Intel Microprocessors (1/7)
Intel 8086
  16-bit registers and 16-bit data bus
  20-bit address bus
    Physical Address Space = 220 bytes = 1MB
Intel 8087
  Floating point co-processor
  Uses segmentation and real-address mode to address memory
  Intel 8088Each segment can address 216 bytes = 64 Kbytes
  Uses 8-bit data bus
  … that’s why less expensive

## Slide 37: Evolution of Intel Microprocessors (2/7)
Intel 80286
  24-bit address bus so
    Physical Address Space = 224 bytes = 16 MB
Intel 80386
  First 32-bit processor with 32-bit general purpose registers
  32-bit data bus and 32-bit address bus so
    Physical Address Space = 232 bytes = 4GB

## Slide 38: Evolution of Intel Microprocessors (3/7)
Intel 80486, introduced in 1989
  Improved version of 80386
  On-chip Floating Point Unit
  On-chip unified Instruction/Data cache of 8 KB
  Introduced the concept of Pipelining
Pentium (80586), introduced in 1993
  32-bit address bus
  64-bit internal data path (inside a processor)
  Superscalar performance: can execute two instructions in one clock cycle
  Separate 8KB instruction and 8KB data caches

## Slide 39: Evolution of Intel Microprocessors (4/7)
Pentium Pro, introduced in 1995
  Three-way superscalar: can execute 3 instructions per clock cycle
  36-bit address bus  up to 64 GB of physical address space
  Introduced dynamic execution
    Out-of-order execution
  Integrated a 256 KB second level L2 cache on chip
Pentium II was introduced in 1997
  Added MMX instructions
Pentium III was introduced in 1999
  Added SSE instructions and eight new 128-bit XMM registers

## Slide 40: Evolution of Intel Microprocessors (5/7)
Pentium IV is a seventh generation x86 architecture
  New micro-architecture design called Intel Netburst
  Very deep instruction pipeline, scaling to very high frequencies
Intel introduced hyper-threading technology in 2002
  Allowed 2 programs to run simultaneously, sharing resources
Xeon is Intel’s name for its server-class microprocessors
  Xeon chips generally have more cache
  Support larger multiprocessor configurations

## Slide 41: Evolution of Intel Microprocessors (6/7)
Pentium M (Mobile) was introduced in 2003
  Designed for low-power laptop computers
  Modified version of Pentium III, optimized for power efficiency
  Large L2 cache
  Runs at lower clock than Pentium IV but with better performance
Extended Memory 64-bit Technology (EM64T)
  64-bit superset of the IA-32 processor architecture
  64-bit general purpose registers and integer support
  Number of general purpose registers increased from 8 to 64
  64-bit pointers and flat virtual address space
  Large physical address space: up to 240 = 1 Terabyte

## Slide 42: Evolution of Intel Microprocessors (7/7)
CISC – Complex Instruction Set Computer
  Large and complex instruction set
  Variable width instructions
  Requires microcode interpreter
  Example is Intel x86 family
RISC – Reduced Instruction Set Computer
  Small and simple instruction set
  All instructions have the same width
  Simpler instruction formats and addressing modes
  Decoded and executed directly by hardware
  Examples are ARM, MIPS, PowerPC, SPARC etc.

## Slide 43: Outline
Overview of Intel Microprocessors
x86 Memory Management

## Slide 44: x86 Operation Modes
x86 architecture operates in 3 basic different modes
  Protected Mode
    All instructions and features of processor are available
    Programs cannot reference memory outside their segments
    Virtual-8086 is special mode of Protected Mode
  Real-Address Mode
    Programs can have direct access to memory and hardware devices
    … so operating system can crash in this mode
  System Management Mode
    Implemented in processors customized for a particular system setup
    Supports power management and system security

## Slide 45: x86 Memory Management
Memory is managed according to the operation mode
  Real-Address Mode
  Protected Mode

## Slide 46: Real-Address Mode Memory Management
16-bit registers
20-bit address bus
  Physical Address Space = 1MByte
  Linear or Absolute Address range is 00000h to FFFFFh
How 20-bit address can be accommodated in 16-bit Registers?
  Solution lies in Segmented Memory

## Slide 47: Real-Address Mode Memory Management
Programs cannot use linear address directly because of 16-bit registers
Addresses are represented using 2 16-bit registers
  One 16-bit value is called Segment Value which is placed in segment register
  Other 16-bit value is called Offset value

## Slide 48: Segmented Memory Scheme
All memory is divided in 64KBytes segments
Each segment begins at an address having a zero in its last hex digit
  … this zero is omitted when representing segment value in 16-bit registers
    A segment value of E00016 refers to the segment address of E000016
If we have Physical Address Space of 220 bytes, and size of each segment is 64KBytes (216bytes), how many segments do we have?

## Slide 49: Segmented Memory Map
64 KBytes
00000
10000
20000
30000
40000
50000
7000:0000
7000:FFFF
Segment
Offset
017A
7000:017A
F0000
64 KBytes
60000
70000
80000
90000
A0000
B0000
C0000
D0000
E0000
Segment
Offset
7000:017A is called Logical Address
7017A is called Linear/Absolute Address

## Slide 50: 20-bit Linear Address Calculation
Segment value
0
15
Offset value
X
1016
+
20-bit Linear Address in hex
In Hex
In Hex
0
15
How to convert a 16-bitSeg:16-bitOffset logical address into 20-bit linear/absolute address

## Slide 51: Protected Mode Memory Management
Restricts application programs from accessing system hardware
Logical Address consists of
  16-bit segment selector (Segment Registers)
  32-bit offset value
Program’s linear address space is 4GBytes
  What is address bus width?
A typical protected-mode program has three segments
  Code Segment
  Data Segment
  Stack Segment
Segment Registers point to the Segment Descriptor Table
  … Segment Descriptor Tables are created by OS to keep track of individual program segments

## Slide 52: Paging
Paging divides the linear address space into fixed-sized block called pages
IA-32 uses pages of size 4 KB
Pages are allocated space on main memory
  … if main memory is full, then on hard disk
Complete set of pages mapped by OS is called Virtual Memory

## Slide 53: Paging
We want to run many programs in parallel
Main memory may not be enough to load all of them at the same time
Disk storage is cheaper and we have plenty of it
Paging gives an illusion that we have unlimited main memory
The more a program depends on paging, the slower it runs
Higher amount of main memory means less usage of paging