## Slide 1: Computer Performance and Cache Memory
Muhammad Irfan Ishaq

## Slide 2: Book Chapter
“Computer Organization and Architecture”
Author “William Stallings”
8th Edition
Chapter 2
  Section 2.2
Chapter 4
  Section 4.1
  Section 4.2
  Section 4.3

## Slide 3: Designing for Performance
Cost of systems continues to drop whereas performance and capacity continue to rise
Today application programs are very complex and power hungry
  Image processing
  Speech recognition
  Videoconferencing
  Multimedia authoring
  Simulation modeling
We have to see how can we use the microprocessor in a way to utilize all it’s clock cycles

## Slide 4: Microprocessor Speed
Processor is not used at its full throttle always
How to keep processor busy and get maximum out of it?
  Branch Prediction
    Processor predicts which branches or groups of instructions are likely to be executed next
  Data Flow Analysis
    Processor analyzes which instructions are dependent on each other
  Speculative Execution
    Processors execute instructions ahead of their actual appearance in the program execution

## Slide 5: Performance Balance
Processor power has increased rapidly
  … what about the speed of other components of computer?
Slow data transfer rate between main memory and processor
If memory fails to keep pace with processor, the processor has to stall in a wait state

## Slide 6: Processor and Memory Performance Gap

## Slide 7: Some Tips to Increase Speed
How to tackle this problem of speed between processor and main memory?
  Increase data bus size
  Include a cache in DRAM to make it more efficient
  Reduce frequency of memory access
  Increase the interconnect bandwidth between processor and memory

## Slide 8: I/O Device Data Rate

## Slide 9: Improvement in Chip Organization and Architecture
Increase hardware speed of processor
  Shrinking the size of logic gates on processor reduces the propagation delay among them
Increase size and speed of cache that is near to processor
  A portion of processor can be dedicated to cache
Changing the processor organization and architecture that can increase the instruction execution
  Using parallelism

## Slide 10: Memory Hierarchy
Total memory capacity can be visualized as hierarchy of components
As we go down the hierarchy, the following occurs
  Decreasing cost per bit
  Increasing capacity
  Increasing access time
  Decreasing frequency of access of the memory by the processor
Magnetic Tape
Magnetic Disk
CD-ROM
CD-RW
DVD-RW
Off-line Storage
Outboard
Storage
Inboard
Storage
Main Memory
Cache
Regis-ters
Lower cost per Byte
Higher Speed, Smaller Size

## Slide 11: Memory Hierarchy
Main Memory (Primary Storage)
  Only programs and data currently needed by the processor are stored here
Auxiliary Memory (Secondary Storage)
  Devices that provide backup storage
  Magnetic disks and tapes
Cache
  Increases the speed of processing
  Rapid rate and smaller size
  Compensates speed differences between main memory and processor
  Stores segments of programs and data currently in use

## Slide 12: Cache Memory
Small amount of fast memory
Sits between main memory and CPU
May be located on CPU chip
Faster than main memory by a factor of 5 to 10
CPU
Cache
Main Memory
Slow
Fast
Word Transfer
Block Transfer

## Slide 13: Cache Operation
CPU requests contents of memory location
Check cache for this data
If present, get from cache (fast operation)
If not present, read required block from main memory to cache
Then deliver from cache to CPU

## Slide 14: Cache Memory Operation
Receive Address RA from CPU
Load Main Memory block into cache line
Fetch RA word and deliver to CPU
Access Main Memory for block containing RA
Deliver RA word to CPU
Allocate cache line for Main Memory block
Start
Done
Is block containing RA in cache?
RA = Read Address
Yes
No

## Slide 15: Cache Performance
When CPU refers to memory and finds the word in cache, it is said to produce a hit
If not found, it is called miss
Hit Ratio = Number of Hits/Total CPU references to memory

## Slide 16: Elements of Cache Design (1/2)
A few basic design elements to classify and differentiate cache architecture
Cache Address
  Logical
  Physical
Cache Size
Mapping Function
  Direct
  Associative
  Set Associative
Line Size

## Slide 17: Elements of Cache Design (2/2)
Replacement Algorithm
  Least Recently Used (LRU)
  First in First out (FIFO)
  Least Frequently Used (LFU)
  Random
Write Policy
  Write through
  Write back
  Write once
Number of Caches
  Single or two level
  Unified or Split