## Slide 1: Symbolic Constants, Data Related Operators , Directives & Addressing Modes
Muhammad HabibUllah
Habib.Wattoo@nu.edu.pk

## Slide 2: Book Chapter
“Assembly Language for x86 Processors”
Author “Kip R. Irvine”
6th Edition
Chapter 3
  Section 3.5
Chapter 4
  Section 4.3
“Computer Organization and Architecture”
Author “William Stallings”
8th Edition
Chapter 11
  Section 11.1

## Slide 3: Symbolic Constants
Created by associating an identifier with an integer expression or text
Identifier also called symbol
Different from a variable
  Symbols do not reserve storage
  Symbols cannot change at runtime
Symbols can be created by using equal-sign directive, EQU and TEXTEQU directives

## Slide 4: Equal-Sign Directive
Associates a symbol name with an integer expression
At assemble time, all occurrences of name are replaced by expression
Helpful when an expression is used many times in a program
name = expression

## Slide 5: EQU Directive
Associates a symbolic name with an integer expression or some arbitrary text
Three different formats
  name EQU expression
  name EQU symbol
  name EQU <text>
expression must be a valid integer expression
symbol is an existing symbol name
text can be any string

## Slide 6: Some Useful Symbols
Current Location Counter
  $ gives the address of location where used
  self_ptr DW $
Keyboard Definitions
  Numeric keys can also be used by defining symbols
  esc_key = 27
  mov al, esc_key

## Slide 7: Calculating Size of Arrays and Strings
Size of array/string can be calculated with the help of location counter
  arr DB 1, 2, 3, 4, 5
  arr_size = ($ – arr)

## Slide 8: Operators and Directives
Operators and Directives are not executable instructions
Different MASM operators and directives to get information about the addresses and size of data
  OFFSET
  PTR
  TYPE
  LENGTHOF
  SIZEOF

## Slide 9: OFFSET Operator (1/2)
This operator returns the offset of a data label
Offset is the distance in bytes, of label from the beginning of data segment
DS
var
Offset
.data
…
var DB 10
…

## Slide 10: OFFSET Operator (2/2)
.data
…
var DB 10
…
.code
…
mov esi, OFFSET var
…

## Slide 11: PTR Operator (1/2)
Sometimes source and destination in an assembly instruction have different types
How to handle this situation?
PTR moves first X bytes from Y into dest
  X is an assembly directive like DB, DW etc.
  Y is source operand
mov dest, X PTR Y

## Slide 12: PTR Operator (2/2)
x86 processors store data in little endian format
So lower addressed byte in memory contains least significant byte of data
PTR moves the first byte of var into al which is 80h in this case
.data
var DW 9A80h
.code
mov al, DB PTR var

## Slide 13: TYPE Operator
Returns the size of a single element of a variable in bytes
.data
var1 DB 9Ah
var2 DD 9A80h
TYPE var1
TYPE var2
Returns 1
Returns 4

## Slide 14: LENGTHOF Operator
Returns the number of elements in array or string appearing on the first line
.data
arr DB 9Ah, 0Ch, 81h
str DB “Hello”,0
LENGTHOF arr
LENGTHOF str
Returns 3
Returns 6

## Slide 15: SIZEOF Operator
Returns total size in bytes of a variable, array or string
Total size is obtained by multiplying TYPE with LENGTHOF values of a variable or array
.data
arr DW 109Ah, 6B0Ch, 2681h
str DB “Hello World!”,0
SIZEOF arr
SIZEOF str
Returns 6
Returns 13

## Slide 16: LABEL Directive
Can be used to give a group name to some variables
Inserts a label with a size attribute without allocating any storage
.data
lab LABEL DB
var DW 1234h
.code
mov al, lab
al contains 34h
Why 34h, and not 12h?

## Slide 17: ALIGN Directive (1/2)
Used to align a variable on 1, 2, 4 or 16 bytes
Why align?
  Because CPU can process data stored at even-numbered addresses more quickly
.data
a DB ?
b DW ?
c DB ?
d DD ?
0000
0001
0003
0005
Address

## Slide 18: ALIGN Directive (2/2)
How to align previous data on even addresses?
.data
a DB ?
ALIGN 2
b DW ?
c DB ?
ALIGN 2
d DD ?
0000
0002
0004
0006
Address

## Slide 19: Calculate Addresses…
Write down the addresses of these data
.data
a DB ?
ALIGN 2
b DB ?
ALIGN 4
c DW ?
ALIGN 2
d DD ?
ALIGN 8
e DW ?
0000
Address

## Slide 20: Addressing Modes
The set of mechanism by which an instruction can specify how to obtain its operands
An operand address provides the location where the data to be processed is stored
In an assembly instruction, the destination may be a register or memory location
Source may be an immediate value or the address of the source data

## Slide 21: Addressing Modes
Immediate
Direct
Indirect
Register
Register Indirect
Displacement
Stack

## Slide 22: Useful Notations
In the next slides, we use the following notations
  A denotes the contents of an address field in the instruction
  R denotes the contents of an address field in the instruction that refers to a register
  EA is the actual effective address of the location containing the referenced operand
  [X] denotes the contents of memory location X or register X

## Slide 23: Immediate Addressing (1/2)
Simplest form of addressing where operand value is present in the instruction
No memory reference other than instruction fetch is required to obtain the operand
 | Operand
Operand = A

## Slide 24: Immediate Addressing (2/2)
Example
.code
MOV AL, 10h

## Slide 25: Direct Addressing (1/3)
Direct access to the data segment is required in direct addressing mode
Address field contains the effective address of operand
Base address of segment and offset of storage location is required
EA = A

## Slide 26: Direct Addressing (2/3)
 | A
Instruction
Memory
Operand
DS
Offset

## Slide 27: Direct Addressing (3/3)
Example
.data
val DB 10h
.code
MOV al, val
MOV al, [102h] ;same as above

## Slide 28: Indirect Addressing (1/3)
Memory cell pointed by address field contains the address of the operand
One major advantage is to reference more words if address field is less than word length
Indirect addressing can be nested or cascaded
EA = [A]
EA = [[A]]

## Slide 29: Indirect Addressing (2/3)
 | A
Instruction
Memory
Pointer to Operand
DS
Operand

## Slide 30: Indirect Addressing (3/3)
Example
.data
val DB 10h
vptr DW val
.code
MOV si, vptr
MOV al, [si]

## Slide 31: Register Addressing (1/3)
Similar to direct addressing
In this mode, a register contains the operand
Depending upon the instruction, the register may be the first operand, the second operand or both
Processing data between register does not involve memory, so it provides fastest processing of data
EA = R

## Slide 32: Register Addressing (2/3)
 | R
Instruction
Registers
Operand

## Slide 33: Register Addressing (3/3)
Example
.data
val DB 10h
.code
MOV al, ah

## Slide 34: Register Indirect Addressing (1/3)
Similar to direct addressing that offset is combined with base address of DS to get physical address
Operand is in memory cell pointed by contents of register R
Offset lies in a pointer register (BX or BP) or index register (SI or DI)
EA = [R]

## Slide 35: Register Indirect Addressing (2/3)
 | R
Instruction
Registers
Pointer to Operand
Memory
Operand
DS
Offset

## Slide 36: Register Indirect Addressing (3/3)
Example
.data
val DB 10h
.code
MOV si, OFFSET val
MOV al, [si]

## Slide 37: Displacement Addressing (1/2)
In this addressing mode, an instruction has two address fields
Both these values are added to produce the effective address
Displacement addressing can be used as
  Relative Addressing
  Base-Register Addressing
  Indexing
EA = A + [R]

## Slide 38: Displacement Addressing (2/2)
 | R | A
Instruction
Registers
Pointer to Operand
Memory
Operand
DS
Offset

## Slide 39: Relative Addressing
Address of next instruction is added to address field to produce EA
Address of next instruction is got from PC
EA = A + [PC]

## Slide 40: Base-Register Addressing
Register contains the main memory address
Address field contains a displacement from address contained in register
Examples are Segment Registers in x86
EA = A + R

## Slide 41: Indexing
Address field contains the main memory address
Register contains the displacement from the address contained in address field
EA = A + R

## Slide 42: Stack Addressing
Operand is on the top of stack
Operand can be pushed on the stack when it is necessary to save it
Whenever operand is needed, it can be popped from the stack

## Slide 43: Extract of Addressing Modes
Mode | Algorithm | Principal Advantage | Principal Disadvantage
Immediate | Operand = A | No memory reference | Limited operand magnitude
Direct | EA = A | Simple | Limited address space
Indirect | EA = (A) | Large address space | Multiple memory reference
Register | EA = R | No memory reference | Limited address space
Register Indirect | EA = (R) | Large address space | Extra memory reference
Displacement | EA = A + (R) | Flexibility | Complexity
Stack | EA = Top of Stack | No memory reference | Limited applicability