## Slide 1: Shift and Rotate Instructions
Muhammad HabibUllah
habib.wattoo@nu.edu.pk

## Slide 2: Book Chapter
“Assembly Language for x86 Processors”
Author “Kip R. Irvine”
6th Edition
Chapter 7
  Section 7.2
  Section 7.4
Chapter 9
  Section 9.2

## Slide 3: Shift and Rotate Instructions (1/2)
Shifting an operand means moving bits right or left from their original positions inside the operand
Rotating an operand fills the bit positions of empty end with the bits gone out on the other end of operand
Shift and Rotate instructions affect the Carry and Overflow flags
Two ways to shift an operand’s bits
  Logical Shift
  Arithmetic Shift

## Slide 4: Logical Shift
Fills the newly created bit positions with zero
Each bit value is shifted to left or right bit position
1 | 0 | 1 | 0 | 1 | 0 | 1 | 1
Logical Shift Right
by 1 position
0 | 1 | 0 | 1 | 0 | 1 | 0 | 1
CF
1

## Slide 5: Arithmetic Shift
Newly created bit is filled with a copy of sign-bit
Preserves the number’s sign-bit
1 | 0 | 1 | 0 | 1 | 0 | 1 | 1
Arithmetic Shift Right
by 1 position
1 | 1 | 0 | 1 | 0 | 1 | 0 | 1
CF
1

## Slide 6: Shift and Rotate Instructions (2/2)
Instruction Mnemonic | Description
SHL | Shift Left
SHR | Shift Right
SAL | Shift Arithmetic Left
SAR | Shift Arithmetic Right
ROL | Rotate Left
ROR | Rotate Right
RCL | Rotate Carry left
RCR | Rotate Carry Right
SHLD | Double-precision Shift Left
SHRD | Double-precision Shift Right

## Slide 7: SHL Instructions
Performs a logical shift left on the destination operand
Syntax for SHL is
  SHL dest, count
CF
0
SHL reg, imm8
SHL mem, imm8
SHL reg, CL
SHL mem, CL
Same for all shift and rotate instructions

## Slide 8: Fast Multiplication
Shifting left by 1 position generates a number which is 2 times the original operand
Shift left by n position multiplies the operand by 2n
0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
Before
SHL by 1 position
0 | 0 | 0 | 0 | 0 | 1 | 0 | 0

## Slide 9: SHR Instructions
Performs a logical shift right on the destination operand
Highest bit position are filled with zero
Syntax for SHL is
  SHR dest, count
CF
0

## Slide 10: SAL and SAR Instructions
SAL is identical to SHL
SAR performs a right arithmetic shift on the destination operand
CF

## Slide 11: ROL Instructions
Shifts each bit to the left
The highest bit is copied into the CF and into the lowest bit
No bits are lost
CF

## Slide 12: ROR Instructions
Shifts each bit to the right
The lowest bit is copied into the CF and into the highest bit
No bits are lost
CF

## Slide 13: RCL Instruction
Shifts each bit to the left
Copies the carry flag to the LSB
Copies the MSB into carry flag
CF

## Slide 14: RCR Instruction
Shifts each bit to the right
Copies the carry flag to the MSB
Copies the LSB to the carry flag
CF

## Slide 15: SHLD Instruction
Shifts destination operand to a given number of bits to left
Bit positions opened up by the shift are filled by the most significant bits of the source operand
Source operand is not affected
Syntax is
Operand Types
SHLD dest, src, count
SHLD reg16/32, reg16/32, imm8/CL
SHLD mem16/32, reg16/32, imm8/CL

## Slide 16: SHRD Instruction
Shifts destination operand to a given number of bits to the right
Bit positions opened up by the shift are filled by the least significant bits of the source operand
Source operand is not affected
Syntax is
Operand Types
SHRD dest, src, count
SHRD reg16/32, reg16/32, imm8/CL
SHRD mem16/32, reg16/32, imm8/CL

## Slide 17: Integer Multiplication
Integer multiplication in x86 can be performed as a 32-bit, 16-bit or 8-bit operation
The default destination operand in these instructions is the accumulator register (EAX/AX/AL)

## Slide 18: MUL Instruction (1/2)
Used to multiply unsigned numbers
The multiplier and multiplicand must be the same size and product is twice their size
MUL instruction has a single operand which is multiplier
MUL reg/mem8 ;AX = AL * 8-bit reg/mem
MUL reg/mem16 ;DX:AX = AX * 16-bit reg/mem
MUL reg/mem32 ;EDX:EAX = EAX * 32-bit reg/mem

## Slide 19: MUL Instruction (2/2)
Multiplicand | Multiplier | Product
AL | 8-bit reg/mem | AX
AX | 16-bit reg/mem | DX:AX
EAX | 32-bit reg/mem | EDX:EAX
MUL sets the CF and OF if upper half of product is non-zero
When AL is multiplied with an 8-bit value, CF and OF are set if AH is non-zero

## Slide 20: IMUL Instruction
Used to multiply signed numbers
Preserves sign by extending highest bit of lower half of the product into the upper bits of product
Three formats of the IMUL instruction
  One-operand format
  Two-operand format
  Three-operand format
IMUL reg/mem ;AX = AL * reg/mem
IMUL reg, reg/mem ;AX = reg * reg/mem
IMUL reg, reg/mem, imm ;reg = reg/mem * imm

## Slide 21: DIV Instruction
Used to divide unsigned integers
Performs 8-bit, 16-bit and 32-bit integer division
Takes only one operand which is the divisor
DIV reg/mem8
DIV reg/mem16
DIV reg/mem32
Dividend | Divisor | Quotient | Remainder
AX | 8-bit reg/mem | AL | AH
DX:AX | 16-bit reg/mem | AX | DX
EDX:EAX | 32-bit reg/mem | EAX | EDX

## Slide 22: IDIV Instruction
Used to divide signed numbers
Uses same operand types as DIV instruction
Before executing 8-bit division, the dividend (AX) must be completely sign-extended using
  CBW (Convert Byte to Word)
  CWD (Convert Word to Double-word)
  CDQ (Convert Double-word to Quad-word)
Remainder has the same size as dividend

## Slide 23: Sign Extension Instructions
CBW
  Extends the sign-bit of AL into AH
CWD
  Extends the sign-bit of AX into DX
CDQ
  Extends the sign-bit of EAX into EDX
MOV AL, -8 ;AL=1111 1000
CBW ;AX=1111 1111 1111 1000
MOV AX, -8 ; AX=1111 1111 1111 1000
CWD ; AX=1111 1111 1111 1000
; DX=1111 1111 1111 1111

## Slide 24: Extended Addition and Subtraction
Extended precision addition/subtraction helps add/subtract numbers having almost unlimited size
ADC helps to add two numbers using the carry flag
SBB helps to subtract two numbers using borrow from carry flag

## Slide 25: ADC Instruction
Adds both a source operand and the value of CF to a destination operand
Instruction format and limitations are same as that of ADD instruction
MOV DL, 0
MOV AL, 0FFh
ADD AL, 0FFh ;AL=FEh, CF=1
ADC DL, 0 ;DL:AL=01FEh

## Slide 26: SBB Instruction
Subtracts both a source operand and value of CF from a destination operand
Possible operands are same as for the SUB instruction
MOV AH, 7
MOV AL,1
SUB AL, 2 ;AL=FFh, CF=0
SBB AH, 0 ;AH:AL=07FFh

## Slide 27: String Instructions (1/2)
Five groups of instructions for processing array of Bytes, Words and Double-words
Called String Primitives but not limited to character arrays only
These instructions use ESI/SI and EDI/DI registers to address memory
Array indexes are repeated and incremented automatically

## Slide 28: String Instructions (2/2)
Instruction | Description
MOVSB, MOVSW, MOVSD | Copy data from memory addressed by SI to memory addressed by DI
CMPSB, CMPSW, CMPSD | Compare the contents of memory addressed by SI to memory addressed by DI
SCASB, SCASW, SCASD | Compare the accumulator register (AL, AX or EAX) to the contents of memory addressed by DI
STOSB, STOSW, STOSD | Store the contents of accumulator register into memory location addressed by DI
LODSB, LODSW, LODSD | Load the contents of memory addressed by SI into the accumulator register

## Slide 29: Direction Flag
String instructions increment/decrement SI and DI based on the state of Direction Flag
DF can be explicitly modified using instructions
  CLD ;clear Direction Flag (forward direction)
  STD ;set Direction Flag (reverse direction)
Value of DF | Effect on SI and DI | Address Sequence
Clear | Increment | Low-High
Set | Decrement | High-Low
if(DF=0) then
SI=SI+1
DI=DI+1
else
SI=SI-1
DI=DI-1
end if

## Slide 30: Repeat Prefix
REP (a repeat prefix) can be used just before MOVSB, MOVSW, MOVSD
By default CX controls the number of repetitions
Prefix | Description
REP | Repeat while CX>0
REPZ, REPE | Repeat while ZF=1 and CX>0
REPNZ, REPNE | Repeat while ZF=0 and CX>0

## Slide 31: REP Prefix
Repeat while CX>0
Value of CX is checked before execution of instruction
If CX is zero, string instruction is not executed
while(CX≠0)
execute the string instruction
CX = CX – 1
end while

## Slide 32: REPE, REPZ Prefixes
while(CX≠0)
execute the string instruction
CX = CX – 1
if (ZF=0) then
exit loop
end if
end while

## Slide 33: REPNE, REPNZ Prefixes
while(CX≠0)
execute the string instruction
CX = CX – 1
if (ZF=1) then
exit loop
end if
end while

## Slide 34: MOVSB, MOVSW, MOVSD (1/2)
Copy data from memory location pointed to by SI to memory location pointed to by DI
SI and DI are either incremented or decremented based on the value of DF
SI/DI incremented/decremented by
  1 when used with MOVSB
  2 when used with MOVSW
  4 when used with MOVSD

## Slide 35: MOVSB, MOVSW, MOVSD (2/2)
.data
src DB “Hello World!”
src_len DB $-src
dst DB src_len DUP(?)
.code
MOV CX, src_len
MOV SI, OFFSET src
MOV DI, OFFSET dst
REP MOVSB

## Slide 36: CMPSB, CMPSW, CMPSD (1/2)
Compare memory operand pointed to by SI to memory operand pointed to by DI
SI and DI are either incremented or decremented based on the value of DF
SI/DI incremented/decremented by
  1 when used with CMPSB
  2 when used with CMPSW
  4 when used with CMPSD

## Slide 37: CMPSB, CMPSW, CMPSD (2/2)
.data
src DB “Hello World!”
src_len DB $-src
dst DB “Hello! World”
.code
MOV CX, src_len
MOV SI, OFFSET src
MOV DI, OFFSET dst
REPE CMPSB

## Slide 38: SCASB, SCASW, SCASD (1/2)
Compare the value in accumulator to the memory value pointed by DI
Useful when looking for a single value in string or array
When combined with REPNE prefix, SCASX scans until either accumulator is matched a value in memory or CX=0
When combined with REPE prefix, string is scanned while CX>0 and value in accumulator matches each subsequent value in string

## Slide 39: SCASB, SCASW, SCASD (2/2)
.data
dst DB “Hello! World”
.code
MOV CX, src_len
MOV DI, OFFSET dst
MOV AL, ‘o’
REPNE SCASB

## Slide 40: STOSB, STOSW, STOSD (1/2)
Store the contents of accumulator in the memory addressed by DI
When used with REP prefix, these instructions can be used to fill all elements of string with the same value

## Slide 41: STOSB, STOSW, STOSD (2/2)
.data
dst DB 5 DUP(?)
dst_len DW $-dst
.code
MOV CX, dst_len
MOV DI, OFFSET dst
MOV AL, ‘H’
REP STOSB

## Slide 42: LODSB, LODSW, LODSD
Load a byte/word from memory at SI into accumulator register
Used to load a single value because older value is always overwritten in accumulator