## Slide 1: Instruction Formats
Muhammad HabibUllah
habib.wattoo@nu.edu.pk

## Slide 2: Book Chapter
“Computer Organization and Architecture”
Author “William Stallings”
8th Edition
Chapter 11
  Section 11.3

## Slide 3: Instruction Format (1/2)
Defines the layout of the bits in an instruction
  Operation Code (opcode)
    Necessary instruction element
    Tells the CPU what to do
  Source/destination Operands
    An instruction can have zero or more operands
    Operands are referenced using one the addressing modes
Basic design issues in Instruction Format are
  Instruction Length
  Allocation of bits

## Slide 4: Instruction Format (2/2)
Simple Instruction Format example
opcode
Operand Reference
Operand Reference
4 bits
6 bits
6 bits
16 bits

## Slide 5: Instruction Length
Instruction Length affects and is affected by
  Memory size
  Memory organization
  Bus structure
  Processor complexity
  Processor speed
Trade off between powerful instruction repertoire and saving space

## Slide 6: Allocation of Bits
More operations in an instruction set requires more opcodes
More opcodes means more bits in opcode field and less bits in operand references
Following factors help to determine the use of addressing bits
  Number of addressing modes
  Number of operands
  Register versus Memory
  Number of register sets
  Address range
  Address granularity

## Slide 7: PDP-8 Instruction Format (1/2)
Memory Reference Instructions
opcode | D/I | Z/C | Displacement
0 |  | 2 | 3 | 4 | 5 |  |  |  |  |  | 11
1 1 0 | Device | opcode
Input/Output Instructions
0 |  | 2 | 3 |  |  |  |  | 8 | 9 |  | 11
D/I = Diret/Indirect Address
Z/C = Page 0 or Current page

## Slide 8: PDP-8 Instruction Format (2/2)
1 1 1 0 | CLA | CLL | CMA | CML | RAR | RAL | BSW | IAC
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11
Register Reference Instructions
1 1 1 0 | CLA | SMA | SZA | SNL | RSS | OSR | HLT | 0
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11
1 1 1 0 | CLA | MQA | 0 | MQL | 0 | 0 | 0 | 1
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11
CLA = Clear Accumulator
CLL = Clear Link
CMA= CoMplement Accumulator
CML= CoMplement Link
RAR= Rotate Accumulator Right
RAL= Rotate Accumulator Left
BSW= Byte SWap
IAC = Increment ACcumulator
SMA= Skip on Minus Accumulator
SZA= Skip on Zero Accumulator
SNL= Skip on Nonzero Link
RSS= Reverse Skip Sense
OSR= Or with Switch Register
HLT= HaLT
MQA=Multiplier Quotient into Accumulator
MQL=Multiplier Quotient Load

## Slide 9: PDP-10 Instruction Format
Opcode | Register | I | Index Register | Memory Address
0 |  |  |  |  |  |  | 8 | 9 |  |  | 12 |  | 14 | 17 | 18 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 35
I = Indirect Bit

## Slide 10: PDP-11 Instruction Format (1/3)
Opcode | Source | Destination
4 | 6 | 6
16-bit instruction formats
Opcode | Offset
8 | 8
Opcode | FP | Destination
8 | 2 | 6
Opcode | R | Source
7 | 3 | 6
Opcode | Destination
10 | 6
Opcode | R
13 | 3
Opcode | CC
12 | 4
Opcode
16
Source and Destination each contain a 3-bit addressing mode and 3-bit
register number
FP indicates one of four floating point registers
R indicates one of the general-purpose registers
CC is the condition code field

## Slide 11: PDP-11 Instruction Format (2/3)
32-bit instruction formats
Opcode | Source | Destination | Memory Address
4 | 6 | 6 | 16
Opcode | R | Source | Memory Address
7 | 3 | 6 | 16
Opcode | FP | Destination | Memory Address
8 | 2 | 6 | 16
Opcode | Destination | Memory Address
10 | 6 | 16

## Slide 12: PDP-11 Instruction Format (3/3)
48-bit instruction formats
Opcode | Source | Destination | Memory Address1 | Memory Address2
4 | 6 | 6 | 16 | 16