## Slide 1: Input/Output
Muhammad HabibUllah
habib.wattoo@nu.edu.pk

## Slide 2: Book Chapter
“Computer Organization and Architecture”
Author “William Stallings”
8th Edition
Chapter 7
  Section 7.1
  Section 7.2

## Slide 3: I/O Problems and Module
Wide variety of peripherals
  Delivering different amounts of data
  At different speeds
  In different formats
All slower than CPU
Need I/O Modules to interact with CPU and Memory
  Interface to CPU and Memory
  Interface to one or more peripherals

## Slide 4: Generic Model of I/O Module
Address Lines
Data Lines
Control Lines
I/O Module
System Bus
Links to
Peripheral
Devices

## Slide 5: External Devices
Human-readable
  Screen, Printer, Keyboard
Machine-readable
  Monitoring and control
  Magnetic disks and Tape drives
Communication
  Modem
  Network Interface Card (NIC)

## Slide 6: External Devices Block Diagram
Control Logic
Transducer
Buffer
Control Signals from I/O Module
Status Signals to I/O Module
Data bits to and from I/O Module
Data (Device-unique) to and from environment

## Slide 7: Typical I/O Device Data Rates

## Slide 8: I/O Module Function
Control and timing
  To coordinate the flow of traffic between internal resources and external devices
Processor communication
  Communication between processor and I/O module
Device communication
  Communication between device and I/O module
Data buffering
  Necessary because of different data rates of processor and peripheral
Error detection
  Unintentional changes to the bit pattern are detected

## Slide 9: I/O Steps
CPU checks the status of peripheral by I/O module
I/O module returns status of external device
If ready, CPU requests the data transfer
I/O module obtains a unit of data from external device
Data are transferred from I/O module to the processor

## Slide 10: Block Diagram of an I/O Module
Data Registers
Status/Control Registers
I/O Logic
External device interface logic
External device interface logic
Data lines
Address lines
Control lines
Data
Status
Control
Data
Status
Control
Interface to system bus
Interface to external device