## Slide 1: Programmed I/O
Muhammad HabibUllah
habib.wattoo@nu.edu.pk

## Slide 2: Book Chapter
“Computer Organization and Architecture”
Author “William Stallings”
8th Edition
Chapter 7
  Section 7.3

## Slide 3: I/O Techniques
Three major I/O techniques
  Programmed I/O
  Interrupt-driven I/O
  Direct Memory Access (DMA)

## Slide 4: Programmed I/O
Data are exchanged between the processor and I/O module
Processor takes direct control of I/O operation by executing a program
  Sensing status
  Read/Write commands
  Transferring data
Processor waits for I/O module to complete operation
If processor is faster than I/O module, then much of the processor time is wasted

## Slide 5: Programmed I/O – Details
CPU requests I/O operation
I/O module performs operation
I/O module sets status bits
CPU checks status bits periodically
I/O module does not inform CPU directly
I/O module does not interrupt CPU
CPU may wait or come back later

## Slide 6: I/O Commands
CPU issues address of particular I/O module and external device
CPU issues one of four I/O commands
  Control – used to activate a peripheral and telling what to do e.g. spin up disk, rewind magnetic tape etc.
  Test – checks status e.g. is the device powered on?
  Read – I/O module obtains data from peripheral and places in internal buffer (data register)
  Write – I/O module takes data from data bus and transmits to the peripheral

## Slide 7: Programmed I/O Block Diagram
Issue read command to I/O module
Read status of I/O module
Check status
Read data from I/O module
Write data into memory
Done?
CPU  I/O
I/O  CPU
Error Condition
I/O  CPU
CPU  Memory
Ready
Not ready
No
Yes
Next Instruction

## Slide 8: I/O Mapping (1/2)
Often a one-to-one relationship between I/O related instructions and I/O commands
One or more peripherals connected to each I/O module
Each peripheral has a unique identifier or address
I/O command issued by processor contains the address of desired peripheral
… each I/O module must interpret the address lines to determine if the command contains address of peripheral connected to it

## Slide 9: I/O Mapping (2/2)
When processor, main memory and I/O share a common bus, two modes of addressing are possible
  Memory-mapped I/O
  Isolated I/O

## Slide 10: Memory-mapped I/O
Single address space for memory locations and I/O devices
Processor treats data and status registers of I/O modules as memory locations
With 8 address lines, a total of 28 = 256 memory locations and I/O address can be supported in any combination

## Slide 11: Isolated I/O
Separate address space
Address bus equipped with
  Memory read/write lines to select memory
  Input/Output lines to select I/O module
Command line specifies whether address refers to memory location or I/O device
With 8 address lines
  256 memory locations can be referenced
  256 I/O addresses are supported