## Slide 1: Computer Organization and Assembly Language
Lecture 7 – 8

## Slide 2: Outline
Operand Types
Direct Memory Operands
Data Transfer instructions
INC and DEC Instructions
ADD Instruction
SUB Instruction
NEG Instruction
FLAGS affected by Addition and Subtraction

## Slide 3: Book Chapters
“Assembly Language for x86 processors”
Author “Kip R. Irvine”
6th Edition
Chapter 4
  Section 4.1
  Section 4.2

## Slide 4: Operand Types (1/2)
We know the format of an instruction from previous lectures
[label:] mnemonic [operand] [;comment]
Instructions can have 0 – 3 operands
Operands can be any of
  Register: Name of an x86 register
  Memory: Reference to a memory location
  Immediate value: a numeric literal

## Slide 5: Operand Types (2/2)

## Slide 6: Direct Memory Operand
Name of a variable shows its offset in data segment
        .data
        var DB 10h
        .code
        mov al, var
If var is stored at address 00000001h, when assembled, above code produces following machine instruction
A0 00000001

## Slide 7: MOV Instruction (1/2)
Copies data from a source operand to a destination operand
First operand is the destination and second operand is the source
MOV dest, src

## Slide 8: MOV Instruction (2/2)
Some rules to follow when using MOV
  Both operands must have same size
  Both operands cannot be memory operands
  CS, EIP, IP cannot be destination operands
  An immediate value cannot be moved to a segment register
Some useful variants of MOV
MOV reg, reg
MOV reg, mem
MOV reg, imm
MOV mem, reg
MOV mem, imm

## Slide 9: Zero/Sign Extension of Integers (1/4)
MOV cannot copy data directly from a smaller operand to a larger one
Suppose we want to move a byte variable var into a 16-bit register ax
    .data
    var DB 10h
    .code
    MOV ax, 0
    MOV al, var

## Slide 10: Zero/Sign Extension of Integers (2/4)
What happens if same approach is followed to copy a negative number?
What is the value in ax after this code is assembled?
What happened to -8?
.data
svar DB -8
.code
MOV ax, 0
MOV al, svar
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0
248

## Slide 11: Zero/Sign Extension of Integers (3/4)
How about doing like this?
.data
svar DB -8
.code
MOV ax, 0FFFFh
MOV al, svar
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0
-8

## Slide 12: Zero/Sign Extension of Integers (4/4)
These examples show different approaches for signed and unsigned number
  In case of unsigned numbers, a zero is extended to all higher order bits of the destination operand
  In case of signed numbers, the sign-bit is extended to all higher order bits of the destination operand

## Slide 13: MOVZX Instruction (1/2)
MOVZX (MOVe with Zero-eXtend) copies the source operand into destination operand and extends zeroes in the remaining higher order bits of destination operand
It has three variants
  MOVZX reg32, reg/mem8
  MOVZX reg32, reg/mem16
  MOVZX reg16, reg/mem8

## Slide 14: MOVZX Instruction (2/2)
.data
val DB 11000011b
.code
MOVZX ax, val
1 | 1 | 0 | 0 | 0 | 0 | 1 | 1
0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 1

## Slide 15: MOVSX Instruction (1/2)
MOVSX (MOVe with Sign-eXtend) copies the source operand into destination operand and extends the sign-bit in remaining higher order bits in destination operand
It has three formats
  MOVSX reg32, reg/mem8
  MOVSX reg32, reg/mem16
  MOVSX reg16, reg/mem8

## Slide 16: MOVSX Instruction (2/2)
.data
val DB 11000011b
.code
MOVSX ax, val
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 1
1 | 1 | 0 | 0 | 0 | 0 | 1 | 1
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 1
0 | 1 | 0 | 0 | 0 | 0 | 1 | 1
.data
val DB 01000011b
.code
MOVSX ax, val

## Slide 17: Practice Problem 1
Determine the status of EAX after every instruction
  .data
  oneByte DB 78h
  oneWord DW 1234h
  oneDword DD 12345678h
  .code
  mov eax,0
  mov al,oneByte
  mov ax,oneWord
  mov eax,oneDword
  mov ax,0
; EAX = 00000000h
; EAX = 00000078h
; EAX = 00001234h
; EAX = 12345678h
; EAX = 12340000h

## Slide 18: XCHG Instruction (1/2)
XCHG instruction exchanges the contents of two operands
This instruction has three different variants
  XCHG reg, reg
  XCHG reg, mem
  XCHG mem, reg
The rules for operands in the XCHG instruction are the same as those for the MOV instruction, except that XCHG does not accept immediate operands

## Slide 19: XCHG Instruction (2/2)
Here are some examples to use XCHG instruction
  xchg ax,bx ; exchange 16-bit regs
  xchg ah,al ; exchange 8-bit regs
  xchg var1,bx ; exchange 16-bit mem op with BX
  xchg eax,ebx ; exchange 32-bit regs
To exchange two memory operands, a register is used as temporary container
  mov ax,val1
  xchg ax,val2
  mov val1,ax

## Slide 20: Direct-Offset Operands (1/2)
Adding a displacement or offset to the name of a variable
This technique makes it possible to access memory locations which do not have explicit labels
For example, to access individual elements of an array

## Slide 21: Direct-Offset Operands (2/2)
  .data
  arr DB 1, 2, 3, 4, 5
  .code
  MOV al, arr ; mov 1 in al
  MOV ah, arr+1 ; mov 2 in ah
  .data
  arr DW 1, 2, 3, 4, 5
  .code
  MOV ax, arr ; mov 1 in ax
  MOV ax, arr+2 ; mov 2 in ax

## Slide 22: Practice Problem 2
Determine the status of registers after the execution of each instruction
.code
  mov bx,0A69Bh
  movzx eax,bx
  ; EAX = 0000A69Bh
  movzx edx,bl
  ; EDX = 0000009Bh
  movzx cx,bl
  ; CX = 009Bh

## Slide 23: Practice Problem 3
Determine the status of registers after the execution of each instruction
.code
  mov bx,0A69Bh
  movsx eax,bx
  ; EAX = FFFFA69Bh
  movsx edx,bl
  ; EDX = FFFFFF9Bh
  mov bl,7Bh
  movsx cx,bl
  ; CX = 007Bh

## Slide 24: Practice Problem 4
Determine the status of registers after the execution of each instruction
  .data
  val1 DW 1000h
  val2 DW 2000h
  .code
  mov ax,val1
  ; AX = 1000h
  xchg ax,val2
  ; AX=2000h, val2=1000h
  mov val1,ax
  ; val1 = 2000h

## Slide 25: Practice Problem 5
Determine the status of registers after the execution of each instruction
  .data
  arrayB DB 10h,20h,30h,40h,50h
  .code
  mov al,arrayB
  ; AL = 10h
  mov al,[arrayB+1]
  ; AL = 20h
  mov al,[arrayB+2]
  ; AL = 30h

## Slide 26: Practice Problem 6
Determine the status of registers after the execution of each instruction
  .data
  arrayD DD 10000h,20000h
  .code
  mov eax,arrayD
  ; EAX = 10000h
  mov eax,[arrayD+4]
  ; EAX = 20000h
  mov eax,[arrayD+4]
  ; EAX = 20000h

## Slide 27: INC and DEC Instructions (1/2)
INC instruction increments 1 in a single operand
DEC instruction decrements 1 from a single operand
Syntax is
  INC reg/mem
  DEC reg/mem
Flags affected
  OF, SF, ZF, AF, PF

## Slide 28: INC and DEC Instructions (2/2)
  .data
  a DB 10h
  .code
  INC a
  MOV al, a
  DEC al
; a = 11h
; al = 10h

## Slide 29: ADD Instruction
Adds a source operand into a destination operand
Both operands must have the same size
Sum is stored in the destination operand
Syntax is
ADD dest, src
Flags affected
  CF, ZF, SF, OF, AF, PF

## Slide 30: SUB Instruction
Subtracts a source operand from a destination operand
Both operands must have the same size
Result is stored in the destination operand
Syntax is
SUB dest, src
Flags affected
  CF, ZF, SF, OF, AF, PF

## Slide 31: NEG Instruction
Reverses the sign of a number by taking its 2’s complement
Syntax is
  NEG reg
  NEG mem
Flags affected
  CF, ZF, SF, OF, AF, PF

## Slide 32: Flags Affected by Addition and Subtraction
Status flags reflect the outcome of an arithmetic or logic instruction
  based on the contents of destination operand
Essential flags are
  ZF
    set when destination operand equals zero
  SF
    set when destination operand is negative
  CF
    set when unsigned value is out of range
  OF
    set when signed value is out of range
MOV instruction never affects the flags

## Slide 33: Zero Flag (ZF)
ZF is set when the result of an operation produces zero in the destination operand
Remember that
  A flag is set when it equals 1
  A flag is clear when it equals 0
MOV al, 1
SUB al, 1
MOV bl, 0FFh
INC bl
INC bl
;no flag affected
;al=0  ZF=1
;no flag affected
;bl=0  ZF=1
;bl=1  ZF=0

## Slide 34: Sign Flag (SF)
SF is set when destination operand is –ve
SF is clear when destination is +ve
MOV al, 0
SUB al, 1
ADD al, 2
;no flag affected
;al=-1  SF=1
;al=1  SF=0

## Slide 35: Carry Flag (CF)
CF is set when result of an arithmetic operation generates an unsigned value that cannot fit into destination operand
MOV al, 0FFh
ADD al, 1
MOV al, 0
SUB al, 1
;no flag affected
;al=00h  CF=1
;no flag affected
;al=0FFh  CF=0

## Slide 36: Overflow Flag (OF) (1/2)
OF is set when the result of a signed arithmetic operation overflows or underflows the destination operand
MOV al, +127
ADD al, 1
MOV al, -128
SUB al, 1
;no flag affected
;al=??  OF=1
;no flag affected
;al=??  OF=1

## Slide 37: Overflow Flag (OF) (2/2)
When adding two integers, remember that OF is only set when
  Two positive operands are added and their sum is negative
  Two negative operands are added and their sum is positive
Overflow never occurs when the signs of two addition operands are different.